## Slide 1: Design of Digital Circuits Lecture 23a: More Caches
Prof. Onur Mutlu
ETH Zurich
Spring 2019
17 May 2019

## Slide 2: Readings
Caches
Required
  H&H Chapters 8.1-8.3
  Refresh: P&P Chapter 3.5
Recommended
  An early cache paper by Maurice Wilkes
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.

## Slide 3: Recall: Cache Structure
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
(stores
memory
blocks)
Hit/miss?
Data

## Slide 4: Recall: Set Associativity
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
SET
Hit?

## Slide 5: What’s In A Tag Store Entry?
Valid bit
Tag
Replacement policy bits
Dirty bit?
  Write back vs. write through caches

## Slide 6: Handling Writes (I)
  When do we write the modified data in a cache to the next level?
    Write through: At the time the write happens
    Write back: When the block is evicted
  Write-back
    + Can combine multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through
    + Simpler
    + All levels are up to date. Consistency: Simpler cache coherence because no need to check close-to-processor caches’ tag stores for presence
    -- More bandwidth intensive; no combining of writes

## Slide 7: Handling Writes (II)
Do we allocate a cache block on a write miss?
  Allocate on write miss: Yes
  No-allocate on write miss: No
Allocate on write miss
  + Can combine writes instead of writing each of them individually to next level
  + Simpler because write misses can be treated the same way as read misses
  -- Requires transfer of the whole cache block
No-allocate
  + Conserves cache space if locality of writes is low (potentially better cache hit rate)

## Slide 8: Handling Writes (III)
What if the processor writes to an entire block over a small amount of time?
Is there any need to bring the block into the cache from memory in the first place?
Why do we not simply write to only a portion of the block, i.e., subblock
  E.g., 4 bytes out of 64 bytes
  Problem: Valid and dirty bits are associated with the entire 64 bytes, not with each individual 4 bytes

## Slide 9: Subblocked (Sectored) Caches
Idea: Divide a block into subblocks (or sectors)
  Have separate valid and dirty bits for each subblock (sector)
  Allocate only a subblock (or a subset of subblocks) on a request
++ No need to transfer the entire cache block into the cache
(A write simply validates and updates a subblock)
++ More freedom in transferring subblocks into the cache (a cache block does not need to be in the cache fully)
  (How many subblocks do you transfer on a read?)
-- More complex design
-- May not exploit spatial locality fully
tag
subblock
v
subblock
v
subblock
v
d
d
d

## Slide 10: Instruction vs. Data Caches
Separate or Unified?
Pros and Cons of Unified:
  + Dynamic sharing of cache space: no overprovisioning that might happen with static partitioning (i.e., separate I and D caches)
  -- Instructions and data can thrash each other (i.e., no guaranteed space for either)
  -- I and D are accessed in different places in the pipeline. Where do we place the unified cache for fast access?
First level caches are almost always split
  Mainly for the last reason above
Higher level caches are almost always unified

## Slide 11: Multi-level Caching in a Pipelined Design
First-level caches (instruction and data)
  Decisions very much affected by cycle time
  Small, lower associativity; latency is critical
  Tag store and data store accessed in parallel
Second-level caches
  Decisions need to balance hit rate and access latency
  Usually large and highly associative; latency not as important
  Tag store and data store accessed serially
Serial vs. Parallel access of levels
  Serial: Second level cache accessed only if first-level misses
  Second level does not see the same accesses as the first
    First level acts as a filter (filters some temporal and spatial locality)
    Management policies are therefore different

## Slide 12: Cache Performance

## Slide 13: Cache Parameters vs. Miss/Hit Rate
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 14: Cache Size
Cache size: total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit and miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data the executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 15: Block Size
Block size is the data that is associated with an address tag
  not necessarily the unit of transfer between hierarchies
    Sub-blocking: A block divided into multiple pieces (each w/ V/D bits)
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks  less
    temporal locality exploitation
  waste of cache space and bandwidth/energy
  if spatial locality is not high
hit rate
block
size

## Slide 16: Large Blocks: Critical-Word and Subblocking
Large cache blocks can take a long time to fill into the cache
  fill cache line critical word first
  restart cache access before complete fill
Large cache blocks can waste bus bandwidth
  divide a block into subblocks
  associate separate valid and dirty bits for each subblock
  Recall: When is this useful?
tag
subblock
v
subblock
v
subblock
v
d
d
d

## Slide 17: Associativity
How many blocks can be present in the same index (i.e., set)?
Larger associativity
  lower miss rate (reduced conflicts)
  higher hit latency and area cost (plus diminishing returns)
Smaller associativity
  lower cost
  lower hit latency
    Especially important for L1 caches
Is power of 2 associativity required?
associativity
hit rate

## Slide 18: Classification of Cache Misses
Compulsory miss
  first reference to an address (block) always results in a miss
  subsequent references should hit unless the cache block is displaced for the reasons below
Capacity miss
  cache is too small to hold everything needed
  defined as the misses that would occur even in a fully-associative cache (with optimal replacement) of the same capacity
Conflict miss
  defined as any miss that is neither a compulsory nor a capacity miss

## Slide 19: How to Reduce Each Miss Type
Compulsory
  Caching cannot help
  Prefetching can: Anticipate which blocks will be needed soon
Conflict
  More associativity
  Other ways to get more associativity without making the cache associative
    Victim cache
    Better, randomized indexing
    Software hints?
Capacity
  Utilize cache space better: keep blocks that will be referenced
  Software management: divide working set and computation such that each “computation phase” fits in cache

## Slide 20: How to Improve Cache Performance
Three fundamental goals
Reducing miss rate
  Caveat: reducing miss rate can reduce performance if more costly-to-refetch blocks are evicted
Reducing miss latency or miss cost
Reducing hit latency or hit cost
The above three together affect performance

## Slide 21: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 22: Software Approaches for Higher Hit Rate
Restructuring data access patterns
Restructuring data layout
Loop interchange
Data structure separation/merging
Blocking
…

## Slide 23: Restructuring Data Access Patterns (I)
Idea: Restructure data layout or data access patterns
Example: If column-major
  x[i+1,j] follows x[i,j] in memory
  x[i,j+1] is far away from x[i,j]
This is called loop interchange
Other optimizations can also increase hit rate
  Loop fusion, array merging, …
Poor code
for i = 1, rows
for j = 1, columns
sum = sum + x[i,j]
  Better code
  for j = 1, columns
  for i = 1, rows
  sum = sum + x[i,j]

## Slide 24: Restructuring Data Access Patterns (II)
Blocking
  Divide loops operating on arrays into computation chunks so that each chunk can hold its data in the cache
  Avoids cache conflicts between different chunks of computation
  Essentially: Divide the working set so that each piece fits in the cache
Also called Tiling

## Slide 25: Restructuring Data Layout (I)
Pointer based traversal (e.g., of a linked list)
Assume a huge linked list (1B nodes) and unique keys
Why does the code on the left have poor cache hit rate?
  “Other fields” occupy most of the cache line even though rarely accessed!
struct Node {
struct Node* next;
int key;
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access other fields of node
}
node = nodenext;
}

## Slide 26: Restructuring Data Layout (II)
Idea: separate frequently-used fields of a data structure and pack them into a separate data structure
Who should do this?
  Programmer
  Compiler
    Profiling vs. dynamic
  Hardware?
  Who can determine what is frequently used?
struct Node {
struct Node* next;
int key;
struct Node-data* node-data;
}
struct Node-data {
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access nodenode-data
}
node = nodenext;
}

## Slide 27: Multi-Core Issues in Caching

## Slide 28: Caches in a Multi-Core System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 29: Caches in Multi-Core Systems
Cache efficiency becomes even more important in a multi-core/multi-threaded system
  Memory bandwidth is at premium
  Cache space is a limited resource across cores/threads
How do we design the caches in a multi-core system?
Many decisions
  Shared vs. private caches
  How to maximize performance of the entire system?
  How to provide QoS to different threads in a shared cache?
  Should cache management algorithms be aware of threads?
  How should space be allocated to threads in a shared cache?

## Slide 30: Private vs. Shared Caches
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 31: Resource Sharing Concept and Advantages
Idea: Instead of dedicating a hardware resource to a hardware context, allow multiple contexts to use it
  Example resources: functional units, pipeline, caches, buses, memory
Why?
+ Resource sharing improves utilization/efficiency  throughput
  When a resource is left idle by one thread, another thread can use it; no need to replicate shared data
+ Reduces communication latency
  For example, data shared between multiple threads can be kept in the same cache in multithreaded processors
+ Compatible with the shared memory programming model

## Slide 32: Resource Sharing Disadvantages
Resource sharing results in contention for resources
  When the resource is not idle, another thread cannot use it
  If space is occupied by one thread, another thread needs to re-occupy it
- Sometimes reduces each or some thread’s performance
- Thread performance can be worse than when it is run alone
- Eliminates performance isolation  inconsistent performance across runs
- Thread performance depends on co-executing threads
- Uncontrolled (free-for-all) sharing degrades QoS
- Causes unfairness, starvation
Need to efficiently and fairly utilize shared resources

## Slide 33: Private vs. Shared Caches
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 34: Shared Caches Between Cores
Advantages:
  High effective capacity
  Dynamic partitioning of available cache space
    No fragmentation due to static partitioning
    If one core does not utilize some space, another core can
  Easier to maintain coherence (a cache block is in a single location)
Disadvantages
  Slower access (cache not tightly coupled with the core)
  Cores incur conflict misses due to other cores’ accesses
    Misses due to inter-core interference
    Some cores can destroy the hit rate of other cores
  Guaranteeing a minimum level of service (or fairness) to each core is harder (how much space, how much bandwidth?)

## Slide 35: Cache Coherence

## Slide 36: Cache Coherence
Basic question: If multiple processors cache the same block, how do they ensure they all see a consistent state?
P1
P2
x
Interconnection Network
Main Memory
1000

## Slide 37: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
1000
1000

## Slide 38: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
ld r2, x
1000
1000
1000

## Slide 39: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
add r1, r2, r4
st x, r1
ld r2, x
1000
1000
2000

## Slide 40: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
add r1, r2, r4
st x, r1
ld r2, x
1000
1000
2000
ld r5, x
Should NOT load 1000

## Slide 41: Design of Digital Circuits Lecture 23a: More Caches
Prof. Onur Mutlu
ETH Zurich
Spring 2019
17 May 2019

## Slide 42: Cache Examples: For You to Study

## Slide 43: Cache Terminology
Capacity (C):
  the number of data bytes a cache stores
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 44: How is data found?
Cache organized into S sets
Each memory address maps to exactly one set
Caches categorized by number of blocks in a set:
  Direct mapped: 1 block per set
  N-way set associative: N blocks per set
  Fully associative: all cache blocks are in a single set
Examine each organization for a cache with:
  Capacity (C = 8 words)
  Block size (b = 1 word)
  So, number of blocks (B = 8)

## Slide 45: Direct Mapped Cache

## Slide 46: Direct Mapped Cache Hardware

## Slide 47: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
47

## Slide 48: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 3/15 = 20%
Temporal Locality Compulsory Misses
48

## Slide 49: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
49

## Slide 50: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 10/10 = 100%
Conflict Misses
50

## Slide 51: N-Way Set Associative Cache

## Slide 52: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
52

## Slide 53: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 2/10
= 20%
Associativity reduces conflict misses
53

## Slide 54: Fully Associative Cache
No conflict misses
Expensive to build
54

## Slide 55: Spatial Locality?
Increase block size:
  Block size, b = 4 words
  C = 8 words
  Direct mapped (1 block per set)
  Number of blocks, B = C/b = 8/4 = 2
55

## Slide 56: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
56

## Slide 57: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 1/15
= 6.67%
Larger blocks reduce compulsory misses through spatial locality
57

## Slide 58: Cache Organization Recap
Main Parameters
  Capacity: C
  Block size: b
  Number of blocks in cache: B = C/b
  Number of blocks in a set: N
  Number of Sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1
58

## Slide 59: Capacity Misses
Cache is too small to hold all data of interest at one time
  If the cache is full and program tries to access data X that is not in cache, cache must evict data Y to make room for X
  Capacity miss occurs if program then tries to access Y again
  X will be placed in a particular set based on its address
In a direct mapped cache, there is only one place to put X
In an associative cache, there are multiple ways where X could go in the set.
How to choose Y to minimize chance of needing it again?
  Least recently used (LRU) replacement: the least recently used block in a set is evicted when the cache is full.

## Slide 60: Types of Misses
Compulsory: first time data is accessed
Capacity: cache too small to hold all data of interest
Conflict: data of interest maps to same location in cache
Miss penalty: time it takes to retrieve a block from lower level of hierarchy

## Slide 61: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
61

## Slide 62: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
62